10949 E. Crystal Falls Pkwy.

Leander, TX  78641

(512) 528-9501

Fax:  (512) 528-9429

DAC viMate©

Q. 		What is DAC viMate©

A.   	DAC viMate© is custom interface software developed using National Instruments LabVIEW8.5 software that interfaces with a Fanuc Robot to remotely update registers, execute program and monitors position.

Q. 		How does DAC viMate© differ from the standard robot software.

A. 	DAC viMate© is a LabVIEW based custom application to interface with Fanuc Robot Controller

  - Remote update of generic registers

  - Remote update of position registers X,Y,Z,w,p,r

  - Modification of point-to-point speed and acceleration deceleration.

  - Remote Program Selection & Execution

  - Control the number of program execution cycles

  - Pause/Resume between program execution

Test sequencing remote start/stop

HMI and messaging interface

Alarm and error messaging indication

Robot position indication

Q.		What is required?

A.		Fanuc Robotics 6-axis Robot with controller

PCDK Run-Time License for communication between LabVIEW controller and robot controller

Pentium based computer with MS Win XP Pro OS

Monitor

USB Keyboard and mouse

Custom national Instruments LabVIEW control application

Ethernet communication to robot controller

One Robot Digital Output driving a relay to interface with work cell system

Convenient remote E-Stop button for safety shut down

Safety switch and safety controller for work cell that is hardwired to the robot safety circuit and monitored by control application.

Fanuc Robot Teach Pendant

LabVIEW based custom application to interface with Fanuc Robot

For additional questions and information about DAC viMate© please contact Design & Assembly Concepts, Inc. at 512 528-9501 or email info@dac-us.com